## Slide 1: The Role of Performance
Chapter - 2

## Slide 2: Chapter - 2
Discusses how to measure, report, and summarize performance and
Describe the major factors that determine the performance of a computer.

## Slide 3: Why examining performance is important?
Hardware performance is often key to the effectiveness of an entire system.

## Slide 4: Why assessing the performance is challenging?
The scale and intricacy of modern software systems, together with the wide range of performance improvement techniques employed by hardware designers have made performance assessment much more difficult.
For different types of applications, different performance metrics may be appropriate and different aspects of a computer system may be the most significant in determining overall performance.

## Slide 5: Defining Performance
$
$
$
$
Running a program on two different workstations
Better

## Slide 6: Defining Performance
Response Time / Execution Time : the time between the start and completion of a task.

## Slide 7: Defining Performance
B
A
N
L
G
B
Time Shared Computer
A
N
G
L
A
1 sec/op
1 sec/op (V)
2 sec/op (C)
Better

## Slide 8: Defining Performance
Response Time / Execution Time : the time between the start and completion of a task.
Throughput : the total amount of work done in a given time.

## Slide 9: Throughput and Response Time
Do the following changes to a computer system increase throughput, decrease response time, or both?
  Replacing the processor in a computer with a faster version – both.
  Adding additional processors to a system that uses processors for separate tasks – throughput (also response time).
Changing either R.T. or T.P. often affect the other.

## Slide 10: Throughput and Response Time
Performance of X is greater than the performance of Y
PerformanceX > PerformanceY
X is faster than Y
1 | > | 1
Execution timeX |  | Execution timeY
Execution timeY | > | Execution timeX
PerformanceX = | 1
 | Execution timeX

## Slide 11: Throughput and Response Time
X is n times faster than Y, it means,
PerformanceX | = | n
PerformanceY |  | 
PerformanceX | = | Execution timeY | = n
PerformanceY |  | Execution timeX | 

## Slide 12: Relative performance
Example: If machine A runs a program in 10 seconds and machine B runs the same program in 15 seconds, how faster is A than B?
  A is n times faster than B if
  A is 1.5 times faster than B
PerformanceA | = | n
PerformanceB |  | 
15 | = | 1.5
10 |  | 
 | Execution timeB | = n
 | Execution timeA | 

## Slide 13: Relative performance
We could also say that – Machine B is 1.5 times slower than machine A. since
PerformanceA | = | n
PerformanceB |  | 
PerformanceB | = | PerformanceA
 |  | n

## Slide 14: Measuring Performance
Time is the measure of computer performance.
Program execution time is measured in seconds per program.
Wall-clock time / response time / elapsed time / execution time – total time to complete a task, including - disk accesses, memory access, I/O activity, OS overhead.

## Slide 15: Measuring Performance
CPU execution time / CPU time
is the time the CPU spends computing for a task and does not include time spent waiting for I/O or running other programs.
CPU execution time / CPU time ≤ Response time

## Slide 16: Measuring Performance
User CPU time – the CPU time spent in the program
System CPU time – the CPU time spent in the OS performing tasks on behalf of the program
CPU time
User CPU time
System CPU time

## Slide 17: Measuring Performance
Execution Time
CPU time
User CPU time
System CPU time
For I/O and Others

## Slide 18: Measuring Performance
Example:
Unix time command –
90.7u 12.9s 2:39 65%
User CPU time
(90.7 seconds)
System CPU time
(12.9 seconds)
Elapsed time
2*60 + 39 = (159 seconds)
90.7 + 12.9 | = | 0.65
159 |  | 

## Slide 19: Measuring Performance
System Performance – considering elapsed time on an unloaded system
CPU Performance – considering user CPU time.


## Slide 20: Measuring Performance
Clock cycle – Almost all computers are constructed using a clock that determines when events take place. These discrete time intervals are called clock cycles (ticks / clock ticks / clock periods / clocks / cycles).
Clock rate – Inverse of clock period.

## Slide 21: Relating the Metrics
CPU execution time for a program | = | CPU clock cycle for a program | × | Clock cycle time
CPU execution time for a program | = | CPU clock cycle for a program
 |  | Clock rate
Hardware designer can improve performance by reducing either the length of the clock cycle or the number of clock cycles required for a program.

## Slide 22
Our favorite program runs in 10 seconds on computer A, which has a 400 MHz clock. We are trying to help a computer designer build a machine, B, that will run this program in 6 seconds. The designer has determined that a substantial increase in the clock rate is possible, but this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for this program. What clock rate should we tell the designer to target?

## Slide 23
Given
CPU timeA= 10 seconds
Clock rateA= 400 × 106 cycles/sec

## Slide 24: Improving Performance (Cont.)
CPU clock cycleA = 10 seconds × 400 × 106 cycles/sec
CPU timeA | = | CPU clock cycleA
 |  | Clock rateA
10 Seconds | = | CPU clock cycleA
 |  | 400 × 106 cycles/sec
CPU timeB | = | 1.2 × CPU clock cycleA
 |  | Clock rateB
CPU timeB | = | CPU clock cycleB
 |  | Clock rateB
= 4000 × 106 cycles

## Slide 25: Improving Performance (Cont.)
= 800 MHz
Clock rateB | = | 1.2 × 4000 × 106 cycles
 |  | 6 seconds
Machine B must therefore have twice the clock rate of A to run the program in 6 seconds.
6 seconds | = | 1.2 × 4000 × 106 cycles
 |  | Clock rateB

## Slide 26: Hardware Software Interface
Since Machine had to execute the instructions to run the program, the execution time must depend on the number of instructions in a program.
CPU clock cycles (for a program) | = | Instructions for a program | × | Average clock cycles per instruction
CPI

## Slide 27: Using the Performance Equation
Suppose we have two implementations of the same instruction set architecture. Machine A has a clock cycle time of 1 ns and a CPI of 2.0 for some program, and machine B has a clock cycle time of 2 ns and a CPI of 1.2 for the same program. Which machine is faster for this program, and by how much?

## Slide 28: Continuation
Let the number of instructions of the program be I
CPU clock cyclesA = I × 2.0
CPU clock cyclesB = I × 1.2
CPU timeA = CPU clock cyclesA × Clock cycle timeA
= I × 2.0 × 1 ns = 2I ns
CPU timeB = I × 1.2 × 2 ns = 2.4I ns
CPU performanceA | = | Execution timeB | × | 2.4I ns | = 1.2
CPU performanceB |  | Execution timeA |  | 2I ns | 
A is 1.2 times faster than B

## Slide 29: Continuation
Basic performance equation
CPU time | = | Instruction count × CPI
 |  | Clock rate
CPU time = Instruction count × CPI × clock cycle time

## Slide 30: Continuation
Sometimes it is possible to compute the CPU clock cycles by looking at the different types of instructions and using their individual clock cycle counts.
CPU clock cycle =  (CPIi × Ci)
Ci – No. of instructions of class i
CPIi – CPI for instruction class i
i = 1
n

## Slide 31: Comparing Code Segments
Example
  The hardware designer supplied:
  Two code sequences requires the following:
  Which code sequence executes the most instructions?
  Which will be faster?
  What is the CPI for each sequence?
Instruction Class | CPI for this class
A | 1
B | 2
C | 3
Code Sequence | Instruction Counts for instruction class |  | 
 | A | B | C
1 | 2 | 1 | 2
2 | 4 | 1 | 1

## Slide 32: Solution
Sequence 1 executes 2 + 1 + 2 = 5 instructions.
Sequence 2 executes 4 + 1 + 1 = 6 instructions.
So sequence 2 executes most instructions.

## Slide 33: Solution
CPU clock cycle =  (CPIi × Ci)
CPU clock cycles1 = (2×1) + (1×2) + (2×3) = 2 + 2 + 6 = 10 cycles
CPU clock cycles2 = (4×1) + (1×2) + (1×3) = 4 + 2 + 3 = 9 cycles
So code sequence 2 is faster.

## Slide 34: Solution
CPI1 | = | CPU clock cycles1 | = | 10 | = | 2
 |  | Instruction count1 |  | 5 |  | 
CPI2 | = | CPU clock cycles2 | = | 9 | = | 1.5
 |  | Instruction count2 |  | 6 |  | 
When comparing two machines, we must look at all three components, which combine to form execution time.

## Slide 35: MIPS
Million instruction per second
MIPS | = | Instruction count |  |  |  | 
 |  | Execution time x 106 |  |  |  | 

## Slide 36: Example patterson 268 page
Execution time | = | CPU clock cycle
 |  | Clock rate
CPU clock cycle =  (CPIi × Ci)

## Slide 37: MIPS as performance measure Example
Code Form | Instruction Counts for instruction class(in billions) |  | 
 | A | B | C
Compiler 1 | 5 | 1 | 1
Compiler 2 | 10 | 1 | 1
Instruction Class | CPI for this class
A | 1
B | 2
C | 3
Assume that the computer’s clock rate is 4 GHz. Which code sequence will execute faster according to MIPS? According to execution time?